## Slide 1
Two-Family Units (Duplexes)
January 17, 2024
Zoning Text Amendment

## Slide 2: Windows and Transparency – 15%
The principal and recessed facade shall include a minimum solid to void ratio of 15%.
Solid means the area calculated by multiplying the width of the front facing facade by the height measured between the foundation and roof line, not including a gable area.

## Slide 3: Solid to Void Analysis
Void means the area calculated by adding the area of all window and door openings in the primary facade of a building, measured around the perimeter of the frame. A front facing window or door shall be included in the void area regardless of its location.
[Garages are not included]
Void to Solid Ratio = 18%
Void to Solid Ratio = 25%

## Slide 4: Established Neighborhoods - Pattern Analysis
Evaluate the Block Face – all properties facing one side of a street in a block. May include adjacent properties that are not on the block face, if there are too few examples.

## Slide 5: Replicate Garage/Driveway Pattern
Single-Family “Pattern”
Duplex Application of the “Pattern”
Single-Family “Pattern”
Notes: For NEW Duplexes, replicate existing Garage/Driveway Pattern that occurs as a predominant feature within the block face
Front-Loaded Garage that does not protrude from the street facing façade-

## Slide 6: Replicate Garage/Driveway Pattern
Single-Family “Pattern”
Duplex Application of the “Pattern”
Single-Family “Pattern”
Notes: For NEW Duplexes, replicate existing Garage/Driveway Pattern that occurs as a predominant feature within the block face
Narrow Drive on one side, accessing Detached Garage in the Rear-

## Slide 7: Replicate Garage/Driveway Pattern
Single-Family “Pattern”
Duplex Application of the “Pattern”
Single-Family “Pattern”
Notes: For NEW Duplexes, replicate existing Garage/Driveway Pattern that occurs as a predominant feature within the block face
Garage in the Rear, accessed from Alley
  708 Brookside, Ames IA (single-family)
  815 3rd Ave SW, Cedar Rapids IA (two-family)

## Slide 8: Roof Patterns - Residential (Ames)
Side Gabled
Hipped with Ridge
Dormers

## Slide 9: Roof Patterns - Residential (Ames)
Dormers
Side Gabled
Front Gabled

## Slide 10: Entry Patterns – Residential (Ames)
Flush
Projecting
Recessed
Projecting Porch with Flush Entry

## Slide 11: Analysis Resources
Helpful in Determining Recesses and Projections

## Slide 12: Neighborhood Analysis

## Slide 13: Visual Examples of Compatible Architecture

## Slide 14: Other Questions?